## Slide 1
CIRCULAR
WASTE-TO-ENERGY SYSTEM FOR FOOD PROCESSING PLANTS
Integrating AD, Biomass Combustion & CHP
Patels Group | Presentation
ERGY8031-1
CAPSTONE - Applied Energy Management

## Slide 2
  Introduction
  Description of Problem
  Objectives
  Proposed design
  Requirements
  Details
  Evaluation of design
  Recomendations
CONTENT

## Slide 3
  Generation: 60 tonnes of organic waste every single day!
  Disposal: Methane emissions and waste valuable energy.
  Our plan: A circular waste-to-energy system using AD + Biomass + CHP.
  Our Goal: Convert waste into electricity, heat, and fertilizer and giving mother earth a high five!
INTRODUCTION

## Slide 4
  Facility relies heavily on natural gas for heat and grid electricity for operations.
  Double cost burden: Paying for disposal + paying for fossil fuel energy.
  Current operation does NOT meet sustainability or decarbonization goals.
Meaning, The plant is wasting energy potential while paying heavily for external energy.
PROBLEM IS...

## Slide 5
  Design an integrated waste-to-energy system
  Renewable electricity (15,000 kWh/day) & Thermal energy (37,000 kWh/day).
  Minimum 60% GHG reduction
  Economic feasibility with a 6.4–9.5 year payback.
  Circular economy principles with digestate fertilizer recovery.
.
OBJECTIVES OF THE PROJECT

## Slide 6
PROPOSED DESIGN
3
CHP
Electricity + Heat
4
Digestate
Fertilizer for Agriculture
2
Biomass Combustion
Thermal Energy
from Dry waste
1
Anarobic Digestion
Biogas
Production
SYSTEM COMPONENT

## Slide 7
ENERGY OUTPUTS
  15,000 kWh/day of renewable electricity generated through CHP
  Significantly reduces dependence on grid electricity
  37,000 kWh/day of usable heat
  Offsets a major portion of natural gas consumption in the plant
Electricity Production
Thermal Energy Production
This combination offsets major portions of the plant’s heat and power demand while creating valuable by-products.
  55 tonnes/day of nutrient-rich digestate
  Can be used as fertilizer, supporting agricultural circularity
Digestate Production

## Slide 8
SUMMARY OF CONSTRAINTS
Performance
Requirement
  Offset 20–30% plant
electricity
  Offset 40–60%
thermal demand
  ≥90% system uptime
Environmental Requirements
  ≥40% GHG reduction
  Must comply with Ontario MOECC, CFIA, and CSA codes
Economic Requirements
  CAPEX ≤ $15M
  Payback < 10 years
  IRR > 8%

## Slide 9
DETAILED DESCRIPTION OF THE DESIGN

## Slide 12
System Integration
  Wet waste → AD
  Dry waste → Biomass boiler
  Biogas → CHP
  Heat loops supply industrial processes
  Digestate → agricultural fertilizer

## Slide 13
1.Anaerobic Digestion (AD)
1,800 m³ CSTR digester
Produces 7,425 m³/day biogas, approx. 58% methane
Digestate is separated into solid + liquid fertilizer streams
2. Biomass Combustion
6 tonnes/day of dry fibrous waste
Produces upto 18,000 kWh/day usable thermal energy
3. CHP System
Converts methane into 15,000 kWh/day electricity
Recovers 19,350 kWh/day heat
Powers plant loads + reduces purchased natural gas

## Slide 14
EVALUATION OF THE DESIGN

## Slide 15
DETAILS
Technical Performance
  Total usable energy: 52,000+ kWh/day
  CHP + biomass meets major plant energy loads
  Technology is fully commercial (TRL 9)
Environmental Impact
  4,000 tonnes CO₂e/year reduction
  47% GHG reduction achieved
  Cuts methane emissions + reduces landfill use

## Slide 18
  Energy savings: $2.17M/year
  Carbon credits: $0.38–0.62M/year
  Net cash flow: $1.55–1.79M/year
  Payback: 6.4–9.5 years
  IRR: 11.8%
FINANCIALS

## Slide 19
  Proceed to detailed engineering design phase
  Conduct waste characterization testing
  Secure carbon credit revenue contracts
  Partner with farms for digestate reuse
  Begin MOECC permitting early
RECOMMENDATIONS

## Slide 20
  The system converts 60 t/day waste into renewable energy effectively.
  Delivers 15,000 kWh electricity + 37,000 kWh heat/day reliably.
  Achieves 47% emission reduction and strong financial returns.
  Provides a scalable, future-proof circular energy model for the food processing industry.
CONCLUSION

## Slide 21
THANK YOU